## Slide 1: Loamy and Clayey Hydric Soil Field Indicators
Lisl Townsend
SJRWMD Soil Scientist
March 21, 2021
Fine Textured Indicators
Field Indicators of Hydric Soils, v. 8.2, 2018

## Slide 2: Loamy and Clayey Soils Notes
Field Indicators of Hydric Soils states on page 21:
All mineral layers above any of the layers meeting the requirements of any F-indicator(s) have a dominant chroma of 2 or less, or the thickness of the layer(s) with a dominant chroma of more than 2 is less than 15 cm (6 inches).
WHAT DOES THIS MEAN?
Basically, above the indicator’s starting depth either:
  There are no mineral soil layers
  All mineral soil above the starting depth has a dominant chroma of 2 or less
  There are less than 6 inches of mineral soil material with a dominant chroma of more than 2 above the starting depth
*Except for F8, F12, F19, F20, F21
Except for F16, nodules and concretions are not considered redox concentrations.

## Slide 3: F2 – Loamy Gleyed Matrix
Is there a layer(s) of loamy very fine sand or finer soil texture in which 60% or more of the layer is a gleyed matrix
Does the layer(s) start < 12 inches from the soil surface
Above the starting depth of this indicator, is either Option A, B, or C satisfied:
  There are no mineral soil layers above this indicator
  All mineral soil above this indicator has a dominant chroma of 2 or less
  There are less than 6 inches of mineral soil material with a dominant chroma of more than 2 above this indicator

## Slide 4: Gleyed Matrix
DEP Data Form Guide
Hues on the Gley 1 page
Above this line are gleyed matrix colors

## Slide 5: F2 – Loamy Gleyed Matrix
Sandy Clay Loam
N 4/ (dark gray)
3 – 13 inches
Fine Mucky Mineral
10YR 2/1 (black)
0 – 3 inches
DEP Photo

## Slide 6: F3 – Depleted Matrix
Is there a layer(s) of loamy very fine sand or finer soil texture with a depleted matrix
Does the layer(s)’s matrix have 60% or more chroma of 2 or less
Does the layer(s) satisfy either Option A or B
  Layer(s) is 2 inches or more thick
  AND
  Starts < 4 inches from the soil surface
  Layer(s) is 6 inches or more thick
  AND
  Starts < 10 inches from the soil surface
Above the starting depth of this indicator, is either Option A, B, or C satisfied:
  There are no mineral soil layers above this indicator
  All mineral soil above this indicator has a dominant chroma of 2 or less
  There are less than 6 inches of mineral soil material with a dominant chroma of more than 2 above this indicator

## Slide 7: F3 – Depleted Matrix
Matrix value of 5 and chroma of 2 or matrix value of 4 and chroma of 2 or less
OR
A, E, or Calcic horizons
THEN
Requires 2% or more redox concentrations occurring as soft masses or pore linings:
Matrix value of 5 or more and chroma of 1 or less or matrix value of 6 or more and chroma of 2 or less
THEN
Does not require 2% or more redox concentrations occurring as soft masses or pore linings
*Not an A, E, or calcic horizons

## Slide 8: F3 – Depleted Matrix
Sandy Clay Loam
10YR 4/1 (dark gray)
Redox concentrations: 25%, 10YR 5/6, diffuse, round
1.5 – 9.75 inches
Sandy Clay Loam
N 3/ (very dark gray)
0 – 1.5 inches

## Slide 9: F6 – Redox Dark Surface
Is there a layer(s) of loamy very fine sand or finer or fine mucky mineral soil texture with distinct or prominent redox concentrations occurring as soft masses and/or pore linings
Does the layer(s) with redox concentrations satisfy either Option A or B
  Layer(s)’s matrix has value of 3 or less and chroma of 1 or less
  AND
  Has 2% or more redox concentrations
  Layer(s)’s matrix has value of 3 or less and chroma of 2 or less
  AND
  Has 5% or more redox concentrations
Is the layer(s) 4 inches or more thick
Does the layer(s) start < 8 inches from the soil surface
Above the starting depth of this indicator, is either Option A, B, or C satisfied:
  There are no mineral soil layers above this indicator
  All mineral soil above this indicator has a dominant chroma of 2 or less
  There are less than 6 inches of mineral soil material with a dominant chroma of more than 2 above this indicator

## Slide 10: F6 – Redox Dark Surface
Redox Concentrations
Sandy Clay Loam
10YR 3/1 (dark gray)
Redox concentrations: 20%, 10YR 5/6, diffuse, round
2.5 – 8 inches

## Slide 11: F7 – Depleted Dark Surface
Is there a layer(s) of loamy very fine sand or finer or fine mucky mineral soil texture with redox depletions (lighter areas associated with redox concentrations)
Do the redox depletions have value of 5 or more and chroma of 2 or less
Does the layer(s) with redox depletions satisfy either Option A or B
  Layer(s)’s matrix has value of 3 or less and chroma of 1 or less
  AND
  Has 10% or more redox depletions
  Layer(s)’s matrix has value of 3 or less and chroma of 2 or less
  AND
  Has 20% or more redox depletions
Is the layer(s) 4 inches or more thick
Does the layer(s) start < 8 inches from the soil surface
Above the starting depth of this indicator, is either Option A, B, or C satisfied:
  There are no mineral soil layers above this indicator
  All mineral soil above this indicator has a dominant chroma of 2 or less
  There are less than 6 inches of mineral soil material with a dominant chroma of more than 2 above this indicator

## Slide 12: F7 – Depleted Below Dark Surface
Sandy Clay Loam
10YR 3/1 (dark gray)
Redox depletions: 30%, 10YR 5/1, diffuse, round
8 – 16 inches
Redox Depletions

## Slide 13: F8 – Redox Depressions
Is the soil profile located within a closed depression subject to ponding
Is there a layer(s) of loamy very fine sand or finer or fine mucky mineral soil texture with 5% or more distinct or prominent redox concentrations occurring as soft masses and/or pore linings
Is the layer(s) 2 inches or more thick
Does the layer(s) start < 4 inches from the soil surface

## Slide 14: F8 – Redox Depressions
Sand
10YR 2/1 (black)
Fill material
0 – 4 inches
Clay
N 2.5/ (black)
Redox concentrations: 15%, 10YR 6/8, diffuse, round
4 – 16 inches
Redox Concentrations

## Slide 15: F10 - Marl
Is the soil profile located with Land Resource Regions U
Is there a layer(s) of marl soil material
Does the layer(s) have value of 5 or more and chroma of 2 or less
Does the layer(s) start < 4 inches from the soil surface

## Slide 16: F10 – Marl
Marl: Calcium carbonate and various amounts of clays and silts
Common calcium carbonate found in marl is calcite.
Calcite forms sedimentary rocks like limestone and chalk.
Soil Taxonomy, 2014
DEP Photo

## Slide 17: F13 – Umbric Surface
Is there a layer(s) of loamy very fine sand or finer or fine mucky mineral or muck soil texture
Is the layer(s) 10 inches or more thick
Does the layer(s) satisfy both Criteria 1 and 2
  The upper 6 inches of the layer(s) has value of 3 or less and chroma of 1 or less
  AND
  The lower 4 inches of the layer(s) has chroma of 2 or less
Does the layer(s) start < 6 inches from the soil surface

## Slide 18: F13 – Umbric Surface
Sand
10YR 2/1 (black)
Fill material
0 – 4 inches
Clay
N 2.5/ (black)
Redox concentrations: 15%, 10YR 6/8, diffuse, round
4 – 16 inches

## Slide 19: THANK YOU